## Slide 1: ROS2
ROS2 패키지, 노드

## Slide 2: ROS2 개발환경 구축
Build System
  Colcon
    Command line tool to improve the workflow of building, testing and using multiple software packages
    Including catkin and ament
    Comparable with ROS 1 and ROS 2
    Workspace
      build: intermediate files are atored Cmake
      install: Each package will be installed
      log: Various logging information
      src: Source codes
.
├── build
├── install
├── log
└── src
4 directories, 0 files

## Slide 3: ROS 패키지
ROS 2의 파일 시스템패키지란?
소프트웨어를 구성하는 기본 단위
구성
  하나 이상의 노드(실행파일)
  package.xml : 패키지에 대한 정보
  Cmakelists.txt : 빌드 설정
  소스파일 :
  환경파일 :
  etc ..
바이너리 설치:
  sudo apt install ros-[] 로 바이너리 설치를 하게 되면 /opt/ros/foxy/… 쪽에 설치가 되게 된다.
소스코드 설치:
  소스코드는 깃에서 클론을 해서 설치하게 되며 자신이 설치하고자하는 워크스페이스에 설치가 되게 된다.

## Slide 4: 개발 환경 설정 .bashrc 파일 설정
Bashrc ( Bourne shell run command) 의 약자로 Steve Bourne 가 제작한 유닉스 오리지널 쉘이다.
  쉘이란 사용자와 커널 사이의 매개체 역할을 하는 프로그램이다. (터미널, terminator.. Etc )
  Bashrc 추가 내용.
개발 툴 설치
  용량 늘리기 20G -> 30G
  source /usr/share/colcon_argcomplete/hook/colcon-argcomplete.bash
  source /usr/share/vcstool-completion/vcs.bash
  source /usr/share/colcon_cd/function/colcon_cd.sh
  export _colcon_cd_root=~/colcon_ws
  alias cbp='colcon build --symlink-install --packages-select'
  alias killgazebo='killall -9 gazebo & killall -9 gzserver & killall -9 gzclient'

## Slide 5: ROS 패키지 생성하기(Python)
ros2 pkg create --build-type ament_python [패키지명] --dependencies [의존성1] [의존성2]…

## Slide 6: Setup.py 작성요령(python)
setup.py
  패키지 안에 있는 코드를 빌드하기 위한 설정 파일

## Slide 7: ROS2 Publisher Node 만들기

## Slide 8: ROS2 subscriber Node 만들기

## Slide 9: ROS 패키지 생성하기(CPP)
ros2 pkg create --build-type ament_cmake [패키지명] --dependencies [의존성1] [의존성2]…
cmake_minimum_required(VERSION 3.8)
project(simple_ros_cpp)
if(CMAKE_COMPILER_IS_GNUCXX OR CMAKE_CXX_COMPILER_ID MATCHES "Clang")
add_compile_options(-Wall -Wextra -Wpedantic)
endif()
# find dependencies
find_package(ament_cmake REQUIRED)
find_package(rclcpp REQUIRED)
find_package(std_msgs REQUIRED)
add_executable(hello_pub src/hello_pub.cpp)
install(TARGETS hello_pub DESTINATION lib/${PROJECT_NAME})
if(BUILD_TESTING)
find_package(ament_lint_auto REQUIRED)
set(ament_cmake_copyright_FOUND TRUE)
set(ament_cmake_cpplint_FOUND TRUE)
ament_lint_auto_find_test_dependencies()
endif()
ament_package()

## Slide 10: ROS 패키지 생성하기(CPP)
ros2 pkg create --build-type ament_cmake [패키지명] --dependencies [의존성1] [의존성2]…
cmake_minimum_required(VERSION 3.8)
project(simple_ros_cpp)
if(CMAKE_COMPILER_IS_GNUCXX OR CMAKE_CXX_COMPILER_ID MATCHES "Clang")
add_compile_options(-Wall -Wextra -Wpedantic)
endif()
# find dependencies
find_package(ament_cmake REQUIRED)
find_package(rclcpp REQUIRED)
find_package(std_msgs REQUIRED)
add_executable(hello_pub src/hello_pub.cpp)
install(TARGETS hello_pub DESTINATION lib/${PROJECT_NAME})
if(BUILD_TESTING)
find_package(ament_lint_auto REQUIRED)
set(ament_cmake_copyright_FOUND TRUE)
set(ament_cmake_cpplint_FOUND TRUE)
ament_lint_auto_find_test_dependencies()
endif()
ament_package()

## Slide 11: ROS 패키지 생성하기(CPP)
hello.cpp
#include <iostream>
using namespace std;
int main()
{
cout << "Hello, World!" << endl;
return 0;
}

## Slide 12
ROS2 관련 자료 모음
Useful ROS Links
The ROS Wiki: https://wiki.ros.org
The ROS Website: https://www.ros.org (Branding)
The OpenRobotics Website: https://www.openrobotics.org (Branding)
The ROSCon Website: https://roscon.ros.org
The ROS Documentation Site: http://docs.ros.org
The Gazebo Website: http://gazebosim.org
The Ignition Robotics Website: https://ignitionrobotics.org
The Autoware Website: https://www.autoware.org
The ROS 2 Design: http://design.ros2.org/
The ROS 2 Documentation: https://index.ros.org/doc/ros2/
The Latest ROS 1 and 2 News and Discussions: https://discourse.ros.org
The Metrics Information of ROS: https://metrics.ros.org
The Answers and Questions for ROS: http://answers.ros.org/questions/
The Awesome ROS 2: https://fkromer.github.io/awesome-ros2/

## Slide 13
ROS2 관련 자료 모음
Development and Package Tools
The Official Docker Images: https://hub.docker.com/r/osrf/ros2/
The ROS Build Farm:
  http://build.ros.org
  http://build.ros2.org/ (DEV)
The ROS Package Repository: http://packages.ros.org (DEV)
The Status Page for Each Distro of ROS:
  ROS 1 Kinetic: http://repositories.ros.org/status_page/ros_kinetic_default.html
  ROS 2 Humble: https://repo.ros2.org/status_page/ros_humble_default.html
  Static Index for Known ROS Packages for Searching and Visualization: https://index.ros.org